BDM generic protocol
Copyright (c) 2013, 2014, 2015, 2016 Olivier TARTROU – olivier.tartrou@gmail.com
This document is licensed under a Creative Commons Attribution 4.0 International License.
# Layers of the generic protocol
The generic protocol is made of the following layers (from lowest to highest):
- electrical connectors;
- electrical interface;
- media layer;
- media driver;
- media driver escape;
- flow control;
- frame bounds;
- escape protocol;
- frame structure;
- applicative layer;
- anti-replay;
- delivery guarantee;
- transactions;
- media access;
- session;
- API;
- application.

Some of these layers are optional, depending on the media layer and the optional features of the generic protocol.
# Electrical connectors
[DE-9] (aka. DB-9)

[8P8C socket] (aka. RJ45)

[USB 2.0 Standard-A]

[USB 3.1 Standard-A]

[USB 2.0 Standard-B]

[USB 3.1 Standard-B]

[USB Mini-B]

[USB 2.0 Micro-A]

[USB 3.1 Micro-A]

[USB 2.0 Micro-B]

[USB 3.1 Micro-B]

[USB 2.0 Micro-AB]

[USB 3.1 Micro-AB]

[USB Type-C]

[CUSTOM]

# Electrical interface
[TIA-232-F]
The electrical interface is made of the following signals:
- TD;
- RD;
- RTS (optional, hardware flow control);
- CTS (optional, hardware flow control);
- GND: electrical ground.

Connection scheme:
- TD signal of the node 1 shall be connected to the RD signal of the node 2;
- RD signal of the node 1 shall be connected to the TD signal of the node 2;
- RTS signal of the node 1 shall be connected to the CTS signal of the node 2 (if hardware flow control is used);
- CTS signal of the node 1 shall be connected to the RTS signal of the node 2 (if hardware flow control is used).

[TIA-232-F signaling]

[positive 3.3V signaling]
Signal levels:
- TD: 0, +3.3V, positive logic;
- RD: 0, +3.3V, positive logic;
- RTS: 0, +3.3V, positive logic (if hardware flow control is used);
- CTS: 0, +3.3V, positive logic (if hardware flow control is used).

[TIA-422-B]

[TIA-485-A]

# Media layer
[UART]
The communication uses an asynchronous serial communication scheme. Data to transmit are serialized on the TD line. Received data incommes from the RD line.

On a TIA-232-F/TIA-422-B/TIA-485-A serial line, transmission unit is called a character. As we configure 8 bits by character, a character equals an octet.

Serial communication has the following characteristics on UART level:
- speed: 115200 bit.s-1;
- start bit: 1, logic value: 0;
- data bits: 8;
- parity: even;
- stop bits: 1, logic value: 1;
- idle state between characters: logic value 1.

Bits shall be serialized LSB (Least Significant Bit) first.

Delays:
- inter-character delay: 0 ns (not used);
- inter-frame delay: 0 ns (not used);
- delay between transmit direction and start bit: 0 ns (not used, TIA-485-A specific);
- delay between stop bit and receive direction: 0 ns (not used, TIA-485-A specific);
- delay between request and respond: 0 ns (not used).
# Media driver
[SERIAL]
The media driver provides functions to open the serial port, configure its parameters (speed, number of data bits, parity, number of stop bits, flow control…), and read or write single characters or stream of characters.

[OS SPECIFIC]
The media driver is provided by the BSP ([STM32Cube]) or by the Operating System ([Linux], [Windows]...).
# Media driver escape
[Linux]

# Flow control

# Frame bounds protocol
[SERIAL]
Asynchronous serial media have no content guarantee. Corrupted bytes can be changed or discarded (missing). Thus, it is needed to uniquely identify the start and the end of a frame in case the receiver gets desynchronized.

The frame bound layer:
- uniquely identifies the start of a frame by adding an STX (0x02) character before the frame;
- uniquely identifies the end of a frame by adding an ETX (0x03) character after the frame.

These bytes shall be escaped if found inside the payload of a frame, see below.

On reception, these bytes shall be removed from start and end of frame. On reception, escape marks shall be remove, see below.
# Escape protocol
[SERIAL]
The frames of the generic protocol are prefixed by a unique STX (0x02) character and post-fixed by a unique ETX (0x03) character. To guarantee this unicity, the frame payloads should not contain either STX or ETX characters. To satisfy this condition on indefinite binary payloads, we add an escape protocol.

The escape protocol uses the DLE (0x10) character as escape character. This character is reserved and shall also be escaped if found inside the payload of a frame.

On transmit:
- when a frame contains a STX character, the escape protocol shall prefix it with the DLE character (DLE STX);
- when a frame contains an ETX character, the escape protocol shall prefix it with the DLE character (DLE ETX);
- when a frame contains a DLE character, the escape protocol shall prefix it with the DLE character (DLE DLE).

On receive:
- when the sequence DLE STX is received, the escape character (DLE) shall be removed before passing the frame to the higher layer (we pass STX);
- when the sequence DLE ETX is received, the escape character (DLE) shall be removed before passing the frame to the higher layer (we pass ETX);
- when the sequence DLE DLE is received, the escape character (DLE) shall be removed before passing the frame to the higher layer;
  - Note: only the first DLE shall be removed (we pass DLE);
- when a sequence DLE x is received and x is neither STX, ETX or DLE, the escape protocol shall be reset, the frame bounds procotol shall be reset and an error shall be notified to the higher layer;
- any other character or character sequence shall be passed unchanged to the higher layer.
# Frame structure
The frame structure is made of:
- a header;
- a payload;
- a footer.

The header has a fixed size and is made of:
- a protocol signature (16-bit);
- a frame id (8-bit).

The protocol is made of several applicative frames, identified by the frame id. The structure of the payload depends on the applicative frame. For a specific frame id, the payload has a fixed size. The payload may be empty.

The footer has a fixed size and is made of:
a CRC.

[CRC-16-CCITT]
The CRC is a CRC-16-CCITT. It uses the following parameters:
- width: 16 bits;
- polynomial: 0x1021;
- reflect in: false;
- XOR in: 0xFFFF;
- reflect out: false;
- XOR out: 0x0000.

The CRC shall be computed on all octets of the frame, excluding the prefixed STX, the CRC itself and the postfixed ETX.
# Applicative layer
Dependant on the specific implementation
# Anti-replay
{not implemented yet}
# Delivery guarantee
{not implemented yet}
# Transactions
{not implemented yet}
# Media access
{not implemented yet}
# Session
{not implemented yet}
# API
Dependant on the specific implementation
# Application
The application is beyond the scope of the generic protocol.